## Slide 1: Motivation
Aim to reduce runtime of iterative graph algorithm
= #_of_iterations × runtime_per_iteration
G=(V[], E[])
while !converge(G):
iteration++
for v in V[]:
//do something
A
B
C
D
E
1
1
4
1
5
3
Chart: iterations
| 0 | 1 | 2 | 3 | 4
系列 1 | 5 | 3 | 2 | 1 | 0
Bellman-Ford
Dijkstra
Fewer iterations,
Higher runtime per iteration
GraphABCD: Scaling Out Graph Analytics with Asynchronous Block Coordinate Descent
Notes: Hi, my name is Yifan Yang. I’m going to present our paper GraphABCD: Scaling Out Graph Analytics with Asynchronous Block Coordinate Descent.
In this paper we aim to reduce the runtime of iterative graph algorithm.
A pseudocode of iterative graph algorithm is shown on the right. For every iteration, it traverses all of the vertices in the graph and perform some computation on the graph. The algorithm terminates if a convergence criteria is met.
Therefore, the runtime of iterative graph algorithm can be roughly decomposed into two parts. Number of iterations times runtime per iteration.
Different implementations of the same iterative graph algorithm exhibits different behaviors on these two components.
We will use single source shortest path as an example.
[click] Suppose we would like to compute the shortest distance with source vertex A.
[click] The bellman-ford variant of SSSP algorithm takes 4 iteration to finish.
The Y axis stands for number of vertices which still haven’t find its shortest path from the source vertex.
[click] However, the Dijkstra implementation of the same algorithm only needs 1 iteration of compute.
[click] Dijkstra has fewer iterations but higher runtime per iteration, because it’s less paralleled than bellman-ford.
How to jointly optimize number of iterations and runtime per iteration systematically is the problem we tackle in this paper.

## Slide 2: Solution: BCD execution model
Aim to reduce runtime of iterative graph algorithm
= #_of_iterations × runtime_per_iteration
G=(V[], E[])
while !converge(G):
iteration++
for v in V[]:
//do something
Solution: introduce Block Coordinate Descent (BCD) execution model, an execution model for optimization algorithm, to graph analytics
Configuring BCD design parameters reduces #_of_iterations
BCD enables efficient asynchronous processing by minimizing synchronization overhead to reduce runtime_per_iteration
GraphABCD: Scaling Out Graph Analytics with Asynchronous Block Coordinate Descent
Notes: [click] Our solution is by introducing a novel execution model block coordinate descent to graph analytics.
Block coordinate descent execution model, or BCD for short, is originally designed for optimization algorithm.
We port BCD to graph domain and leverage its insights to jointly optimize number of iterations and runtime per iteration.
[click] Specifically, theoretical study of BCD from optimization community suggests that we can configure design parameters in BCD model to effectively reduce number of iterations.
[click] Furthermore, BCD execution model intrinsically support asynchronous processing.
This can better utilize the underlying hardware, especially heterogeneous platform, by minimizing synchronization overhead to further reduce runtime per iteration.

## Slide 3
//SSSP Example
G=(V[], E[])
while !converge(G):
b=choose_block(G)
for v in b:
tmp_depth=MAX
for ngh in v.ngh:
tmp_depth=min(tmp_depth,
ngh.depth+distance(v,ngh))
v.depth=tmp_depth
Until Convergence
Partition Graph
Choose Block
Update Block
GraphABCD: Scaling Out Graph Analytics with Asynchronous Block Coordinate Descent
Block Coordinate Descent execution model
Notes: We now introduce how BCD execution model works on graph analytics.
On the top left corner is a flow chart of BCD execution model and the pseudocode of example SSSP algorithm is shown at the bottom.
BCD executes in three stages.
In the first stage, it partitions the graph into multiple blocks. Each vertex is assigned to one block.
In the second stage, the algorithm choose one block from the graph according to some selection rule.
It then traverse every vertex in the block either sequentially or in parallel.
In the final stage, the algorithm computes the new vertex value and updates the block accordingly.
If the vertex values are not converged, it will start a next iteration of choosing and updating blocks until convergence.
By configuring design parameters in this execution model, such as the size of vertex block or the block selection rule, BCD can reduce the number of iterations of graph algorithms.

## Slide 4: GraphABCD framework and evaluation
Prototyped on Intel HARPv2 CPU+FPGA system
Geo-mean speedup of 2.0x on execution time and 4.8x reduction on number of iterations over GraphMat
GraphABCD: Scaling Out Graph Analytics with Asynchronous Block Coordinate Descent
Choose Block
Gather
Until Convergence
Apply
PE
Scatter
Partition Graph
CPU
Compute Intensive
Sequential Access
Accelerator
Control Intensive
Random Access
Notes: We design a graph analytic framework GraphABCD, which implements the asynchronous variant of BCD execution model.
We can exploit asynchronous processing to reduce runtime per iteration.
GraphABCD runs on CPU+accelerator heterogeneous platform.
Thanks to the asynchronous BCD execution model, we are able to cheaply offload the compute-intensive/sequential memory access stages to the accelerator.
And let CPU handle the control-intensive/random memory access stages.
We prototype GraphABCD framework on Intel HARP2 CPU-FPGA heterogeneous system.
Compared with the state of the art GraphMat framework, GraphABCD achieves a geo-mean speedup of 2.0x on execution time and 4.8x reduction on number of iterations.